## Slide 1
Wireless Encryption

## Slide 2: Wireless Encryption
Wireless networks are radio transmitters and receivers
  Shared, accessible medium
    Unlike cable where the medium (cable) is private
For privacy, you must encrypt
Only devices with the key can transmit and receive

## Slide 3: WPA
WiFi Protected Access
WPA was replacement for WEP (Wired Equivalent Privacy), 2002
  Never use WEP
  Underlying security flaws
Quick fix to hold over from WEP to whatever would replace it
WPA: RC4 with TKIP (Temporal Key Integrity Protocol)
  Encrypted hash with larger Initialization Vector (IV)
  Each packet has unique 128-bit encryption key

## Slide 4: TKIP
Temporal Key Integrity Protocol
Mixed the keys
  Combines the secret root key with the Initialization Vector
Adds sequence counter
  Prevent replay attacks
Implements 64-bit Message Integrity Check
  Hard to tamper with in real time
    Take too long and will be too late for sequence counter
TKIP has its own set of vulnerabilities
  Retired 2012

## Slide 5: WPA2 and CCMP
WPA2 certification began in 2004
  AES (Advanced Encryption Standard) replaced RC4 in WPA
  CCMP (Counter Mode with Cipher Block Chaining Message Authentication Mode Protocol) replaced TKIP
CCMP block cipher mode
  AES for data confidentiality
  128-bit key, 128-bit block size
  Requires more computational power
CCMP security services
  Data confidentiality (AES)
  Authentication
  Access control