## Slide 1: Cybersecurity
Wireless Jamming

## Slide 2
Wireless Jam

## Slide 3: Wireless Signals
WiFi is digital radio signals operating at set frequencies
  2.4GHz – 802.11a, 802.11b, 802.11g
  5GHz – 802.11n, 802.11ac
WiFi is controlled radio signals
  Complex signal: Quadrature Amplitude Modulation (QAM)
  Determines bits from the amplitude and phase of signal
  If signal cannot be heard, data transfer is interrupted

## Slide 4: Radio Frequency (RF) Jamming
Transmitting any interfering radio signals
Example:
  Imagine having a conversation with a friend, you’re exchanging ideas for a project, and making really great progress on the assignment.
  Along comes someone that wants to disrupt you. You might normally be able to ignore them or speak over their distractions.
  Then they pull out a pair of crash cymbals.
  The conversation will stop until they stop playing the cymbals.
  This individual has jammed the conversation.
  Radio jamming is very similar.

## Slide 5: Jamming Sources
Unintentional
  Referred to as interference, or RFI
  Microwave oven
  Fluorescent lights
  Nearby cell phone towers
  Licensed radio operators
  Baby monitors
  Electronic arcing
Intentional
  Malicious individual wants to disable your network

## Slide 6: Wireless Jamming
Different modes
  Constant, loud signal (likely RFI or simple jammer)
  Random bits/constant
  Legitimate frames
  Data sent at random times
    Random, nonsense data in legitimate frames
  Reactive jamming
    Only when target tries to communicate
802.11b Signal
Microwave Oven

## Slide 7: Locating the jammer
Radio “Fox hunting”
  Directional antenna
  Attenuator
  Signal strength meter
Location
  Nearby, close proximity
  Someplace with electric power

## Slide 8: Locating the Jammer
Check for RFI
  Intermittent? What appliances are in use?
    Microwave
    Wire/connector lose in refrigerator or HVAC
  Turn off power breakers in that area until RFI stops
    Offending device is on that circuit somewhere
Watch the radio signals
  Make use of RTL-SDR or similar device
  Tune to offending band
  Watch what signals overpower wifi