## Slide 1: Cybersecurity
WPS Attacks

## Slide 2: Using WPS
Wi-Fi Protected Setup
Provides easy setup for joining a device to a network
Different ways to connect:
  Push a button on the access point
  Enter a PIN on access point into device
  Near-field communication (NFC) – bring the mobile device close to access point

## Slide 3: Hacking WPS
PIN is an eight-digit number
  7+1, seven digits followed by a checksum digit
  Seven digits = 10,000,000 possible combinations
  8th digit is computed based on first 7 digits
WPS validates the PIN in halves
  First half: 4 digits (10,000 possibilities: 0000-9999)
  Second half: 3 digits (1,000 possibilities: 000-999)
  Total number of guesses is 11,000 (much less than the original 10,000,000 combinations!)
Automated process will cycle through all 11,000 possible combinations in under 4 hours.

## Slide 4: Protecting WPS PIN
Attacker only needs 11,000 possible guesses
  (4 hours may seem like a long time, but a determined hacker can setup a device and walk away, come back later after it’s cracked it.)
Slow down the amount of time between entries
  Not often a legitimate user will enter wrong PIN multiple times
  More wrong guesses = increased delay between PIN entries
  Make hack take from 4 hours to hundreds or thousands of hours
Intrusion Protection System should alert to too many bad PIN attempts

## Slide 5: Protecting WPS
Pushbutton allows any device to join the network
  Physically protect router or access point
  Do not allow unauthorized users to press the button
  Better: Disable the WPS pushbutton!
WPS PIN may be visible on the access point
  DO NOT keep the default PIN
  Hide the PIN, keep it out of sight
WPS PIN

## Slide 6: Other WPS Attacks
Offline WPS PIN attack
Some chipset manufacturers did not generate true random numbers for generating hashes to encrypt the “WPS Setup”
Attack known as Pixie Dust uses probable hash values to bypass WPS PIN guessing. This is done “offline” and does not hammer the access point.
  PIN attempt slowdowns are useless to this attack
  Cracks faster than 4 hours – usually in seconds or minutes!
Protecting from this? Disable WPS altogether. Don’t use it!