## Slide 1: Cybersecurity
Virtual Private Networks

## Slide 2: VPN
Virtual Private Network
  Encrypted data over untrusted, public network
Concentrator
  Device that handles encryption/decryption
  Sometimes standalone, sometimes integrated in firewall
Hardware- or Software-based
Client software used to connect remotely

## Slide 3: Remote access VPN
Remote device connects to VPN concentrator
  Provides private link to company network from afar
  Trusted connection over untrusted network
Remote Laptop
VPN Concentrator
Company Network
Internet

## Slide 4: SSL VPN (Secure Sockets Layer VPN)
Uses common SSL/TLS protocol (tcp/443)
  Common port, fewer connectivity issues
Authenticates users
  No requirement for digital certificates or shared passwords (like IPSec)
Browser-based or VPN client software

## Slide 5: Full tunnel
Internet
Company Network

## Slide 6: Site-to-Site VPN
Remote Site
Company Network
VPN Concentrator
VPN Concentrator

## Slide 7: IPSec (Internet Protocol Security)
OSI Layer 3 Security
  Encrypts every packet
Confidentiality and integrity
  Encryption and packet signing
    No “replay attack” possible (packets signed and timestamped)
Standardized
  Supported by most vendors
Two underlying IPSec protocols
  Authentication Header (AH)
  Encapsulation Security Payload (ESP)

## Slide 8: Transport mode and tunnel mode
IP Header | Data
IP Header | IPSec Headers | Data | IPSec Trailers
New IP Header | IPSec Header | IP Header | Data | IPSec Trailers
Original Packet:
Transport Mode:
Tunnel Mode:

## Slide 9: Authentication Header (AH)
Hash of the packet and shared key
  MD5, SHA-1, or SHA-2 are common
  Adds the AH to the packet header
New IP Header | AH Header | IP Header | Data
Authenticated
IP Packet with Authentication (tunnel mode)

## Slide 10: Encapsulation Security Payload (ESP)
Encrypts packet
  MD5, SHA-1, or SHA-2 for hash
  3DES or AES for encryption
Adds header, trailer and Integrity Check Value
New IP Header | ESP Header | IP Header | Data | ESP Trailer | Check Val
Encrypted
Authenticated
IPSec Datagram with ESP (tunnel mode)