## Slide 1: Cybersecurity
Router and Switch Security

## Slide 2: Hub
Layer 1 device
Replicates packets to all ports
  No logic involved
Simple, unsophisticated
Does not segment network
Allows for many problems
  Broadcast storms
  Packet collisions
  Network snooping
Hard to find, most devices are switches now

## Slide 3: Switches
Layer 2 device
  Forwards traffic based on MAC address
  Create/store MAC address tables
Physically similar to a hub
  Functionally smarter
Many ports
High throughput

## Slide 4: Routers
Layer 3 Device
Routes traffic between networks
Often connects differing network types
  LAN, WAN, copper, fiber, wireless
Directs traffic based on IP address (Layer 3)

## Slide 5: Layer 3 Switch
Router and switch together in one box
Switching still happens at OSI Layer 2
Routing still happens at OSI Layer 3
Just one box for easier deployment

## Slide 6: Access Control Lists (ACLs)
Rules to allow or deny traffic
  Also used for NAT, QoS, IDS/IPS, etc.
Defined for Incoming or Outgoing ports
ACLs evaluate certain criteria
  Source IP, Destination IP, TCP port, UDP port, ICMP

## Slide 7: Configuring an ACL
192.168.1.15
192.168.1.13
192.168.1.10
192.168.0.1
192.168.0.10
192.168.0.100
192.168.0.101
192.168.0.15
192.168.1.1
192.168.1.18

## Slide 8: Anti-spoofing techniques
Spoofing – using another host’s address
Anti-spoofing prevents many types of attacks
  Man-in-the-middle, DDoS, etc
Detect duplicate MAC addresses/IP addresses
Filtering reserved IP addresses
  Private address should not route to or from internet
Reverse Path Forwarding (RPF)
  Response to inbound packet should return via same path
  If not then drop the packet

## Slide 9: Switch port security
Protection is usually at the perimeter
  Once inside, network is largely wide open
Often easy to get on the network
  Lobby, conference rooms, public meeting spaces
  Protect (and limit) those connections routes
Disable network ports not in use
Disable network drops not in use
Monitor wireless range
  Use minimum power necessary

## Slide 10: Network Access Control (NAC)
IEEE 802.1X – Port-based Network Access Control
  Users must authenticate to get on network
  Use of EAP and RADIUS
    EAP - Extensible Authentication Protocol
    RADIUS - Remote Authentication Dial-In User Service
Disable network ports not in use (physical ports)
Check for duplicate MAC addresses

## Slide 11: Loop Prevention
Connect two switches to each other
  Each will send broadcast traffic back and forth forever
    “That MAC isn’t here, I’m passing it on.” “That MAC isn’t here, I’m passing it on.” “That MAC isn’t here, I’m passing it on.” “That MAC isn’t here, I’m passing it on.”
  Layer 2 has no “counting” mechanism for hops
Easy way to bring down a network
  Easy to resolve, just unplug loop
  Hard to spot
Spanning Tree Protocol
  IEEE Standard 802.1D
  Prevents loops in switched networks
  Even home networking equipment features STP

## Slide 12: STP in action
Switch B
Switch T
Switch Q
Switch H
Switch D
Switch A
Switch G
Switch X

## Slide 13: STP in action
Switch B
Switch T
Switch Q
Switch H
Switch D
Switch A
Switch G
Switch X
LOOP
LOOP
LOOP
LOOP
Lots of loops. Unstable network. Will easily get flooded and crash.

## Slide 14: STP in action
Switch B
Switch T
Switch Q
Switch H
Switch D
Switch A
Switch G
Switch X
STP seeks out other switches downstream and counts hops to that switch. Ports are disabled so no loops exist

## Slide 15: STP in action
Switch B
Switch T
Switch Q
Switch H
Switch D
Switch A
Switch G
Switch X

## Slide 16: STP in action
Switch B
Switch T
Switch Q
Switch H
Switch D
Switch A
Switch G
Switch X
If a link goes down, STP reactivates disabled port so service is uninterrupted.

## Slide 17: Flood guard
Limit number of MAC addresses on an interface
  Only allow specific MAC addresses
Switch monitors number of unique MAC addresses
  Maintains MAC address list
Port security activates after MAC limit is reached
  Lock it down! (Usually disables physical port)