## Slide 1
Access Points

## Slide 2: Access point
Wireless Access Point (WAP)
Layer 2 device
Bridge between wired/wireless networks
Not a wireless router
  Wireless router is both a WAP and a router (Layer 3)
  WAP in a single device
Notes: Q: Why are most WAPs flat and white? A: Usually ceiling mounted in most installations (blends in with ceilings), and since most ceiling are white... Q: Why are most ceilings white? A: _________ ? ____________

## Slide 3: SSID Management
SSID - Service Set Identifier
  Name of the wireless network
  LINKSYS, DEFAULT, NETGEAR
Change SSID to something other than default
Disable SSID broadcasting?
  Never intended as security feature
  SSID can be determined through analyzing wireless traffic
  “Security through obscurity” is not really security

## Slide 4: MAC filtering
Media Access Control
Limits access through hardware address
  Keeps the neighbors, lightweights out
Easy to pull valid MAC addresses through wireless analysis
  Spoof working MAC address and you’re in
“Security through obscurity”

## Slide 5: Power level controls
Use as little power as necessary
What is “necessary”?
  Signal coverage
  User locations
Consider the users’ location
  Where are users typically?
  How far from access point?
  High-gain antennas can help shape direction of signal

## Slide 6: Band selection and bandwidths
Throughput
  Maximum theoretical throughputs
  Actual throughput can vary widely
Frequency
  2.4GHz and 5GHz
  Sometimes both
Distance
  A combination of antennas
Channels
  Differences in geographical location
  Non-overlapping channels would be ideal

## Slide 7: Band selection
 | Throughput* | Frequency
802.11a | 54Mbps | 5GHz
802.11b | 11Mbps | 2.4GHz
802.11g | 54MBps | 2.4GHz
802.11n | 300Mbps / 900Mbps | 2.4GHz / 5GHz
802.11ac | 500Mbps per channel | 2.4GHz / 5GHz
  Maximum theoretical throughputs (Actual throughput may vary)
  Ensure non-overlapping channels are used when possible
    Channels 1, 6, and 11 do not overlap

## Slide 8: Omni directional antennas
Most common
Signal distributed in all directions
Signal radiates and comes in on long side of antenna (not tip)
Good enough for most users
No ability to focus the signal
  Different antenna required to “steer” signal

## Slide 9: Directional antennas
Focus the signal, increase distance
Send and receive in a single direction
Rejects signal in opposite direction
Antenna performance measured in dB
  3dB of gain = 2x power

## Slide 10: Directional antenna types
Patch antenna
  Roughly 180° pattern
  Directional, high gain
Yagi antenna
  Narrow beam
  Very directional, higher gain
Parabolic dish antenna
  Focused signal, down to a single point
  Highly directional, highest gain

## Slide 11: Wireless controllers
Manage WAPs from central location
  Configure and deploy changes to all sites at once
Easy to add more access points
Monitor all wireless activity from one point
Switch
Wireless controller
WAP
WAP
WAP
WAP
WAP

## Slide 12: Wireless configurations
Fat access points
  Access point handles all wireless
  Less administrative load on switch
  More expensive
Thin access points
  Radio transceiver in device and that’s it
  Administrative load is back at switch
  Less expensive