## Slide 1
Mobile Device Connection Methods

## Slide 2: Cellular networks
Mobile devices
  “cellular” phones
Service area divided into “cells”
  Towers cover each cell
  3 towers serve each call
    can triangulate phone’s location
Security concerns
  Traffic monitoring
  Locating tracking
  Worldwide access to a mobile device

## Slide 3: WiFi
Local network access
  Local network security problems
Same security concerns as any other WiFi devices
  Device can capture network data
  Lost phone can carry sensitive data
    Encrypt your data!
  Man-in-the-middle
    Mobile device could sniff network traffic
  Denial of Service
    Frequency interference with company wifi
  “Hotspot” could be Rouge Access Point
    Exfiltrate internal data via cellular

## Slide 4: Satellite Communications
During natural disasters or from remote locations
  Cell towers down or non-existent
Literally talking to space
  Satellites in orbit pass overhead
  Usually Iridium satellites
Voice and data from almost anywhere
Any handheld device could be security risk
  Similar security issues to other smartphones
    Only the service is different

## Slide 5: Near Field Communication (NFC)
Two-way wireless communication
  Extension of one-way RFID
Payment systems use NFC
  Google wallet
  Apple Pay
Bootstrap for other wireless
  NFC helps with Bluetooth pairing
Access token, identity “card”
  Short range with encryption support
  Your phone is the key (Some hotels offer NFC)

## Slide 6: NFC security concerns
Remote capture
  It is a wireless network
  10m range for active devices
Jam known NFC frequencies
  Denial of Service (NFC just won’t work)
Relay / Replay attack
  Man in the Middle
    Attacker “sniffs” NFC traffic and plays it back
Loss of NFC device control
  Stolen/lost phone = Stolen/lose keycard

## Slide 7: ANT/ANT+
Proprietary wireless sensor network protocol
  2.4GHz ISM band (industrial, scientific, medical)
  “Internet of Things” low-power protocol
    Fitness devices
    Heart rate monitors
    Temperature sensors
Separate wireless service
  Not 802.11 or Bluetooth
Denial of Service
  Spectrum jamming
Encryption is optional
  No method to maintain integrity
This is one of several competing IoT protocols. This topic likely to be removed on next Sec+ test update.

## Slide 8: Infrared
Included on many mobile devices
  Less popular these days
File transfers are possible
  Any device within visual distance can “sniff” IR traffic
Other phones can be used to control your IR devices

## Slide 9: Universal Serial Bus (USB)
Physical connectivity to your mobile device
  USB to your computer
  USB, Lightning, or other proprietary connection
  USB-C becoming de facto standard in EU
Physical access is always a concern
  Is that USB port really just power?
A locked device is relatively secure
  Enable auto-lock. If you walk away, it’s safe(r).
Mobile phones can also exfiltrate
  Phone can appear to be USB mass storage device