## Slide 1
Peripheral Security

## Slide 2: Wireless keyboards and mice
Many wireless keyboards and mice communicate in the clear
  Rely on proprietary wireless communication protocols
  Usually 2.4GHz frequency
With a receiver, it’s easy to capture keystrokes
  Tool called “KeySniffer”
  Inject keystrokes and mouse movements wirelessly
  Remotely control the computer
Some keyboards support AES
  Encryption from the keyboard to the computer

## Slide 3: Displays
Electromagnetic radiation
  Information on a screen can generate radio signals (called RF)
  Internal signals of a laptop or external cable
  Eavesdrop through the walls
Firmware hacks
  All displays have chips inside to make them operate
  Those chips rely on firmware (software for the hardware)
  Firmware upgrades usually have no security
  Hacked firmware can
    Log information on the screen
    Ransomware the display (locked until ransom is paid)

## Slide 4: WiFi-enabled SD cards
Combination of SD storage and 802.11 WiFi file transfers
  Allows easy transfer of data from a camera to a computer
SD card authentication vulnerabilities
  Predictable access, known default passwords
  Easy to read files over WiFi
API access to the SD card
  Manufacturer must implement strong security (they usually don’t)
  API access can result in data leakage or data loss for organization

## Slide 5: Printers/Multi-function devices
“All-in-one” multi-function devices
  Printer, scanner, copier, fax all in one box
  Network connectivity
Unauthorized access
Reconnaissance
  Log files for all activity
  Can be used to glean information
Gather organizational information
  Capture spool files
  “What’s been printed?”

## Slide 6: External storage devices
Storage outside the computer, often removable
  Extremely portable, easy to move large data
Limited authentication
  Anyone can connect and read
Often used for exfiltration of data
  Disable USB storage access
    No thumb drives allowed
    No external storage allowed

## Slide 7: Digital cameras
Capture still images and video
  Take pictures of sensitive information
Device operates as external storage
  Easy to move data around for photographers
  Easy to copy data to camera’s storage
    Exfiltrate data through the camera
Camera firmware can be compromised
  Like most firmware updates, there’s often little security
  Security cameras too