## Slide 1
PAP, CHAP, and MS-CHAP

## Slide 2: PPP authentication
Point-to-Point Protocol (PPP)
  Connects two routers directly
    No host in between (No other networks)
Variations of PPP
  Point-to-Point Tunneling Protocol (PPTP)
    Very common for VPNs
  Point-to-Point Protocol over Ethernet (PPPoE)
    Common for DSL Connections
  Point-to-Point over ATM (PPPoA)
    Used with ATMs
Authentication for PPP is provided by:
  PAP
  CHAP
  MS-CHAP

## Slide 3: PAP (password authentication protocol)
A two-way handshake
Username and password sent in plaintext
  No security or encryption
PAP has become an outdated authentication standard
  Still is rarely used

## Slide 4: PAP Authentication
User
PAP Server
Username: JSmith1776
Password: P@ssW0rd1776
Correct! I granted you access!

## Slide 5: CHAP
Challenge-Handshake Authentication Protocol (CHAP)
  Three-way handshake
    Link is established and the server sends a challenge message
    The user sends the username and password (or challenge answer), this is encrypted/hash format when sent back to the server
    The server compares the two hashes
      If they match, they are connected
      If they do not match, the server terminates the session
  Continuous checking
    The server will continuously check to make sure the connection is valid
    The user will not know these checks occur

## Slide 6: CHAP authentication
User
PAP Server
Username: **Encrypted Username**
Password: **Encrypted Hashed Password**
Hash matches the one stored! Access Granted
What is your username and password?

## Slide 7: MS-CHAP
Microsoft Challenge Handshake Authentication Protocol
  Microsoft’s version of CHAP
MSCHAPv1
  Last used with Windows 7
MSCHAPv2
  Current MSCHAP used
  Contains improved cryptographic support