## Slide 1
Chapter 8
Overview of
Network Security and
Network Threats

## Slide 2
Certification Objectives
CompTIA Security+
  1.2 Compare and contrast types of attacks.
  2.2 Given a scenario, use appropriate software tools to assess the security posture of an organization.
  2.6 Given a scenario, implement secure protocols.
  3.2 Given a scenario, implement secure network architecture concepts.

## Slide 3
Certification Objectives (continued)
Microsoft MTA Security Fundamentals
  3.3 Understand protocol security.

## Slide 4
Section 8.1
Network Basics

## Slide 5
Key Terms
ANDing
Classless Internet Domain Resolution (CIDR)
cyclical redundancy check (CRC)
de facto standard
global unicast address
initial sequence number (ISN)
Internet Assigned Numbers Authority (IANA)
Internet Control Message Protocol (ICMP)
Internet Corporation for Assigned Names and Numbers (ICANN)

## Slide 6
Key Terms (continued)
link-local address
local host
Media Access Control (MAC) address
Network Address Translation (NAT)
octet
packet sniffer
proprietary
protocol

## Slide 7
Key Terms (continued)
Regional Internet Registrars (RIRs)
site-local address
socket
subnet mask
three-way handshake
time to live (TTL)
WHOIS

## Slide 8
Learning Goals
Discuss the evolution of networking protocols.
Identify the components of an IPv4 address.
Compare and contrast IPv4 and IPv6 protocols.
Explain TCP and UDP packets.

## Slide 9
TCP/IP Review
Protocol: industry-accepted standardized format that allows communication between devices
Networking protocols allow communication to take place
Proprietary: owned by someone and cannot be used without permission
Proprietary protocols used only for those vendors and their systems

## Slide 10
TCP/IP Review (continued)
Use of Transmission Control Protocol/Internet Protocol (TCP/IP) eventually became necessary
De facto standard: one that is generally accepted over time and adopted for use, but not required
Nearly every network system uses TCP/IP
Two versions: IPv4 and IPv6

## Slide 11
IPv4 Basics
IPv4 Addresses
  Unique value that is assigned to host on a computer network
  Dot-decimal format
  Octet: one of the four 8-bit sections in a TCCP/IP IPv4 address
  Largest value possible in any octet is 255
  Entire address is always 32 bits long

## Slide 12
IPv4 Basics (continued)

## Slide 13
IPv4 Basics (continued)
Network host obtains address manually or automatically
  Manual assignment: static IP address
  Assigned automatically: unique address is received from a server
  IP address serves two purposes:
    Part identifies the network to which the host is assigned
    Remaining portion is unique ID of the host on that network

## Slide 14
IPv4 Basics (continued)
IPv4 Host vs. Network
  Subnet mask: value that, when mathematically compared to the network address, can identify which portion of the IP address is part of the network and which portion identifies the unique host value
  Binary: numbering system that only uses the values of 0 and 1
  Each binary digit represents one bit of information

## Slide 15
IPv4 Basics (continued)

## Slide 16
IPv4 Basics (continued)

## Slide 17
IPv4 Basics (continued)
Classless Internet Domain Resolution (CIDR): way to represent IP addresses in compressed form
  Subnet mask written as a total number of the on bits
  Easier way to visualize subnet mask
  Identifies first number of binary bits in network portion
  255.255.255.0 in decimal; /24 in CIDR

## Slide 18
IPv4 Basics (continued)
To calculate network address portion of 172.16.4.201:
  Convert decimal numbers to binary
  Use ANDing to compare original address to host
    Process of comparing two binary digits and creating a value
    1 AND 1 = 1
    1 AND 0 = 0
    0 AND 0 = 0

## Slide 19
IPv4 Basics (continued)

## Slide 20
IPv4 Basics (continued)
Private, Public, and Special Addresses
  Local host: device on which you are working
  IPv4 uses an address of 127.0.0.1 to represent the local host
  Private address: used on internal network; cannot be used on Internet
  Any IPv4 address that starts with any of these octets is a private address
Class | Private Range
A | 10.x.x.x
B | 172.16.x.x-172.31.x.x
C | 192.168.x.x

## Slide 21
IPv4 Basics (continued)
Network Address Translation (NAT)
  Network service that converts an internal private number to a number for a public network, such as the Internet
  When packet is returned, NAT finds internal reference to private address and converts public address back to private
  Uses unique port number to create unique entry

## Slide 22
IPv4 Basics (continued)
NAT often runs on a router to handle the conversion from private to public address
Socket: IP address and port together
Business gets public IP address from an Internet Service Provider (ISP)

## Slide 23
IPv4 Basics (continued)

## Slide 24
IPv4 Basics (continued)
Internet Assigned Numbers Authority (IANA): organization responsible for the control of IP addresses
Regional Internet Registrars (RIRs): five different registrars for IANA that assign IP addresses

## Slide 25
IPv4 Basics (continued)

## Slide 26
IPv4 Basics (continued)
IP Address Owner
  Important to identify who is behind an IP address
  Internet Corporation for Assigned Names and Numbers (ICANN): maintains the responsibility for managing and coordinating the maintenance of the databases that store this information
  Databases provide information about owner of website

## Slide 27
IPv4 Basics (continued)
IP Address Owner
  WHOIS: system that provides the owner of a domain and a contact person for the domain by querying the ICANN databases
  ICANN and IANA provide management, technical support, and standards behind many of the services and protocols on the Internet

## Slide 28
IPv6 Basics
IPv6 Addresses
  IPv4: 4.3 billion (4,300,000,000) possible addresses
  IPv6: (340,282,366,920,938,463,463,374,607,431,768,211,456) possible addresses
  IPv6 based on hexadecimal or Base 16 numbering system
  System includes value 0-9 and A-F

## Slide 29
IPv6 Basics (continued)

## Slide 30
IPv6 Basics (continued)
Address Meaning
  Length of address increased from 32 bits to 128 bits
  Eight sections of hexadecimal quartets
  Hextets: hexadecimal quartets
  Each hextet represents 16 binary bits
  Sections are separated by a colon (:) instead of a period (.)

## Slide 31
IPv6 Basics (continued)
Address Meaning
  Ex: 2001:203A:0000:0000:5300:0000:0027:8A9C
  Portions of the address indicate network and host address
  First quartet identifies type of IPv6 address
  Address possibly can be shortened

## Slide 32
IPv6 Basics (continued)
Address Meaning
  Remove consecutive sections of zeros and replace with two colons (::)
  Can only be done once in an address hextet or quartet
  Single section of 0000 can become 0
  Leading zeros in quartet can be removed
  Ex: 2001:203A:0000:0000:5300:0000:0027:8A9C (unshortened) 2001:203A::5300:0:27:8A9C (shortened)

## Slide 33
IPv6 Basics (continued)
Hexadecimal Conversion
  Using conversion calculators and basic math, data can be converted from hexadecimal to decimal.
  Hexadecimal 40
    0 is equivalent to 160
    4 is equivalent to 161

## Slide 34
IPv6 Basics (continued)

## Slide 35
IPv6 Basics (continued)
IPv6 Host vs. Network
  First 64 bits of an address identify network
    First 48 bits represent actual network address
    Second 16 bits are subnet mask
  Last 64 bits identify host

## Slide 36
IPv6 Basics (continued)

## Slide 37
IPv6 Basics (continued)
First quartet in section one indicates type of IPv6 address
Three types
  global unicast address
  link-local address
  site-local address

## Slide 38
IPv6 Basics (continued)
Global unicast address:
  Public IPv6 address; can be routed and sent on the Internet
  Most common begin with 2001
Link-local address
  IPv6 address that can be used only on the link or broadcast domain
  Not forwarded through routers

## Slide 39
IPv6 Basics (continued)
Site-local address
  IPv6 address similar to a private address in IPv4
  Cannot be seen on the Internet
  Begins with FEC0
  Special address to designate local host
    0000:0000:0000:0000:0000:0000:0000:0001
    ::1

## Slide 40
IPv6 Basics (continued)

## Slide 41
Packets
Information is often too large to travel as a single unit of data.
Data separated into multiple pieces and encapsulated inside packets and frames.
Important to understand type of data in packets and which packets are part of same transmission

## Slide 42
Packets (continued)
Dissecting IP Packets
  Important to understand construction of IPv4 and IPv6 packets including header information
  Information can be used to analyze traffic, track packets, and search for unusual activity
  Constructed with either TCP or UDP

## Slide 43
Packets (continued)
TCP packets
  Connection-oriented packets
  Contain information that helps ensure reliability of transmission
  Most common type of packet on Internet
  Data broken up into a series of transmissions and identified by tracking properties
  Checksum

## Slide 44
Packets (continued)
UDP packets
  Connectionless protocol packets
  Can be transmitted faster than TCP packets
  UDP does not acknowledge receipt of packets
  Less emphasis placed on reliability

## Slide 45
Packets (continued)
Sent data is packaged into layers

## Slide 46
Packets (continued)
Media Access Control (MAC) addresses: physical addresses embedded into the hardware of network cards
Cyclical redundancy check (CRC): error checking of the frame

## Slide 47
Packets (continued)
TCP segment is created at the Transport layer of the OSI model
  Ports show where data are entering and exiting the system
  Sequence number is 32-bit number used to track how much data are sent
  Acknowledgement field will reflect a value indicating data were successfully received

## Slide 48
Packets (continued)

## Slide 49
Packets (continued)
Flags are 1-bit fields that may signal special conditions in the header
Checksum value used to detect if there was any corruption of sent data

## Slide 50
Packets (continued)

## Slide 51
Packets (continued)
UDP
  UDP is connectionless so less information needs to be sent with data
  Data integrity is still important

## Slide 52
Packets (continued)
Additional Header Information
  Time to live (TTL): value controls how long the packet will search for a destination address before it is deleted
  Internet Control Message Protocol: component of TCP/IP protocol responsible for transmitting messages across networks

## Slide 53
Packets (continued)

## Slide 54
Packets (continued)
Packet Sniffer
  Tool that intercepts raw data traveling on the network media
  Uses network interface card (NIC) to capture data
  May only see traffic to and from host computer or may see all traffic on network segment depending on type and configuration

## Slide 55
Packets (continued)
Packet Sniffer
  Wireless traffic can only be viewed one channel at a time
  Once traffic is found, sniffer reads header information, timing, and sequencing
  Can only read unencrypted data
  Wireshark is well-known, free, open-source sniffer

## Slide 56
Packets (continued)
Three-Way Handshake: sending host and receiving client complete a three-step process to verify the successful transmission of data
    SYN connection (from Host A to Host B)
    SYN/ACK connection (from Host B to Host A)
    ACK connection (from Host A to Host B)

## Slide 57
Packets (continued)
Step 1 SYN Connection
  Sending host (A) will transmit a request to set up a connection to receiving host (B)
  Initial sequence number (ISN): used as part of the transmission process to manage packets within a transmission session

## Slide 58
Packets (continued)

## Slide 59
Packets (continued)
Step 2 SYN/ACK Connection
  Receiving host needs to acknowledge the SYN from sending host
  Acknowledge value increases by 1
  SYN and ACK flags are turned on

## Slide 60
Packets (continued)

## Slide 61
Packets (continued)
Step 3 ACK Connection
  Connection is validating receipt of previous steps and acknowledging transmission
  Resulting return transmission will turn on ACK flag and increment the sequence number by 1

## Slide 62
Packets (continued)

## Slide 63
Section 8.1 Review
Convert the subnet mask of /26 to decimal.
255.255.255.192
Which network service converts a private IP address to a public IP address?
Network Address Translation (NAT)
What can be used to find out the owner of a website?
WHOIS

## Slide 64
Section 8.1 Review
What function creates a value to ensure a frame is not corrupted or damaged?
cyclical redundancy check (CRC)
Which flags are set in the second stage of the three-way handshake?
ACK – Host A to Host B

## Slide 65
Section 8.2
Network Threats

## Slide 66
Key Terms
denial of service (DoS) attack
distributed denial of service (DDoS) attack
File Transfer Protocol/SSL (FTPS)
flood guard
netstat
ping sweep
secure copy protocol (SCP) Secure File Transfer Protocol (SFTP)
secure shell (SSH)
Smurf attack
SYN flood
Telnet

## Slide 67
Learning Goals
Identify preventative measures for denial of service attacks.
Explain the role of ICMP in ping sweeps.
Describe the function of the netstat command.
Discuss security challenges for remote connections.

## Slide 68
Denial of Service Attacks
Denial of service (DoS) attacks: hacks against the availability of data
  Do not destroy or steal data
  Intended to prevent rightful users from accessing systems
Distributed denial of service (DDoS) attack: many hosts are contributing in attacking the victim

## Slide 69
Denial of Service Attacks (continued)

## Slide 70
Denial of Service Attacks (continued)
Smurf Attack: involves overwhelming the victim’s computer with ICMP requests
SYN Flood: involves the hacker exploiting a vulnerability in the three-way handshake by not closing the handshake
  Attacker sends a SYN, target responds with SYN/ACK
  Instead of closing handshake, hacker sends another SYN
  Target responds

## Slide 71
Denial of Service Attacks (continued)

## Slide 72
Denial of Service Attacks (continued)
Protecting Against DoS Attacks
  Much of protection takes place on edge routers or other security appliances using special configurations and access-control lists
  Edge router: separates internal network from public network
  Flood guard: can drop packets or apply filters in place on switchets or routers is a DoS attack is detected

## Slide 73
Denial of Service Attacks (continued)
If IP is not faked or spoofed, IP can be blocked in firewall
Many DoS attacks occur with spoofed IP addresses
Overcome this with a limit on the total number of sessions

## Slide 74
Ping Sweeps
Ping sweep: scans a subnet using ICMP requests to map out valid IP addresses
Helpful to validate IP addresses in use
Hackers can use same information to probe a subnet and find potential targets
Batch file can perform one

## Slide 75
Ping Sweeps (continued)
Advanced IP Scanner and Angry IP Scanner
Both programs offer:
  Remote administration
  Cross-platform capability
  MAC address identification
Installed on computers using access to network and unblocked ICMP connections on hosts

## Slide 76
Netstat Command
Netstat: allows you to view TCP and UDP connections and to further filter the view to ICMP, IPv4, and IPv6
  See statistics and which ports are open, closed, or listening to incoming sessions
  May provide clues to source if you are under attack
  Windows version has switches prefaced with a dash

## Slide 77
Netstat Command (continued)

## Slide 78
Netstat Command (continued)
Output screen lists data in columns
  Proto (name of protocol)
  Local Address (IP address and port number)
  Foreign Address (IP address and port number of remote computer)
  State

## Slide 79
Netstat Command (continued)

## Slide 80
Remote Connections
Allows a person to use another computer as if sitting in front of it
  Telnet
  SSH
Presents security challenges since physical access to machine cannot be controlled

## Slide 81
Remote Connections (continued)
Telnet
  Component of TCP/IP that allows a person to remotely log in to another host on the network
  Text-based interface that uses port 23
  Allows for remote configuration and management
  Seldom used due to vulnerabilities
  Nothing is encrypted during transfer

## Slide 82
Remote Connections (continued)
SSH
  Secure shell (SSH): encrypted interface that uses port 22 for transactions
  Uses public key encryption to authenticate source of data
  Secure copy protocol (SCP): based on SSH to allow the secure copying of files from the local host to the remote host

## Slide 83
Remote Connections (continued)
File Transfer Protocol
  Secure File Transfer Protocol (SFTP): uses a single channel to transmit and receive data
  File Transfer Protocol/SSL (FTPS): has SSH functionality with an added second channel for secure transmissions

## Slide 84
Section 8.2 Review
What security principle is violated in a DoS attack?
availability
Which type of DoS attack exploits the ICMP protocol?
Smurf
Give the command entry to view all Ethernet statistics on the network interface.
netstat

## Slide 85
Section 8.2 Review
Which part of the three-way handshake is not conducted in a SYN flood?
ACK
Which port should be blocked to prevent Telnet traffic?
23