## Slide 1
Chapter 9
Protecting Network
Services and
Infrastructure
from Attacks

## Slide 2
Certification Objectives
CompTIA Security+
  1.2 Compare and contrast the types of attacks.
  2.1 Install and configure network components, both hardware and software based, to support organizational security.
  2.2 Given a scenario, use appropriate software tools to assess the security posture of an organization.
  2.4 Given a scenario, analyze and interpret output from security technologies.
  2.6 Given a scenario, implement secure protocols.
  3.2 Given a scenario, implement secure network architecture concepts.

## Slide 3
Certification Objectives (continued)
Microsoft MTA Security Fundamentals
  3.2 Understand network isolation.
  3.3 Understand protocol security.

## Slide 4
Section 9.1
Network Design

## Slide 5
Key Terms
authoritative DNS server
Challenge Handshake Authentication Protocol (CHAP)
demilitarized zone (DMZ)
DNS local cache
DNS poisoning
DNS Security Extensions (DNSSEC)
Domain Name System (DNS)
Extensible Authentication Protocol (EAP)
extranet
Internet Key Exchange Protocol version 2 (IKEv2)

## Slide 6
Key Terms (continued)
intranet
Layer 2 Tunneling Protocol (L2TP)
MS-CHAP
nonauthoritative DNS server
Password Authentication Protocol (PAP)
perimeter network
Point-to-Point Protocol (PPTP)
Protected EAP (PEAP)
screened subnet
Secure Socket Tunneling Protocol (SSTP)

## Slide 7
Key Terms (continued)
tunneling
virtual local area network (VLAN)
virtual private network (VPN)
VLAN access control list (VACL)
VPN concentrator

## Slide 8
Learning Goals
Evaluate threats to DNS.
Assess network design techniques for isolating segments and improving security.

## Slide 9
DNS Review
Domain Name System (DNS): network service that resolves names on a network, such as web servers or host computer names, to their IP addresses
DNS poisoning: when a valid DNS name is redirected to another site that is likely malicious
DNS local cache: temporary storage location on the local computer

## Slide 10
DNS Review (continued)
Local DNS cache or DNS resolver cache is populated two ways:
  Requests made at the client
  Entries in the local hosts file
    Located c:\windows\system32\drivers\etc\hosts in Windows
    Located /etc/hosts in Linux
    Does not contain any information other than comments
    Automatically loads in local DNS cache when operating system starts

## Slide 11
DNS Review (continued)
Local-Network DNS Cache
  Network servers store DNS information for the local network
  Also store DNS entries for websites to speed up subsequent requests
  Authoritative DNS server: controls the records in the database and provides answers that have configured by an original source

## Slide 12
DNS Review (continued)
Local-Network DNS Cache
  Nonauthoritative DNS server: holds requests from clients for a period of time to speed up subsequent requests and does not contain copies of any domains
  DNS cache can be compromised or poisoned

## Slide 13
DNS Review (continued)

## Slide 14
DNS Review (continued)
Shared DNS Information
  DNS servers get their information from other DNS servers
  Validity of data is only as good as the data themselves
  Corrupted DNS server can compromise unprotected systems
  Ex: data retrieved from Chinese DNS servers temporarily blocked sites such as Facebook, Twitter, and YouTube

## Slide 15
DNS Review (continued)
Things to protect a system from DNS poisoning:
  Install antimalware programs on clients to help prevent DNS cache hijacking
  If using Microsoft Server, store DNS database in Active Directory for additional security
  Limit who has privileges to configure DNS environment and records

## Slide 16
DNS Review (continued)
Things to protect a system from DNS poisoning (continued):
  Consider not hosting local DNS client cache
  Consider configuring DNS Security Extensions (DNSSEC): requires all responses from a DNS server are digitally signed to ensure they come from an authorized source

## Slide 17
Network Design Techniques
Virtual local area network (LAN)
  Logical grouping of hosts that treats them as if they were physically connected
  Security benefits:
    Limits the broadcast of packets to just that network
    Allows traffic from different groups to be separated
    Can separate voice traffic from data traffic

## Slide 18
Network Design Techniques (continued)

## Slide 19
Network Design Techniques (continued)
Another method of VLAN creation is using the host’s MAC address
  More secure than assigning by port
  VLAN assignment can be physically changed
  Does not affect traffic

## Slide 20
Network Design Techniques (continued)
VLANs create virtual subnets
  Allows the VLAN to be further secured
  VLAN access control list (VACL): allows traffic to be filtered within the VLAN
  Different VLANs can be configured with unique VACLs

## Slide 21
Network Design Techniques (continued)
Demilitarized zone (DMZ)
  Segment of a network that allows some public access and borders the private network where the public access is blocked
  Screened subnet or perimeter network: another name for a DMZ
  Typically used for public-facing servers
  Anything in the DMZ is exposed to the Internet

## Slide 22
Network Design Techniques (continued)
DMZs are created by developing borders between the different networks using firewalls
  Type of traffic and hosts that enter DMZ are filtered with the public-facing firewall
  Another firewall borders the DMZ and company private network

## Slide 23
Network Design Techniques (continued)

## Slide 24
Network Design Techniques (continued)
Intranets and Extranets
  Intranet
    Essentially a private Internet environment for internal use only
    Provides a secured environment for forms, information, and portals to other tools

## Slide 25
Network Design Techniques (continued)
Intranets and Extranets
  Extranet
    Extension of an intranet where specific third-party users can be allowed access to a secured intranet
    Ex: vendor or partner needs to access company data

## Slide 26
Network Design Techniques (continued)
VPN
  Needs of remote users need to be considered, but so does security
  Virtual private network (VPN): provides a method to secure data traveling through other networks, such as the Internet
  Tunneling: encrypting data traveling across the remote connection with a VPN

## Slide 27
Network Design Techniques (continued)
Remote-access VPN: allows user to connect to the network using the Internet from a remote client
Site-to-site VPN: allows an organization to connect static or fixed sites to each other using the Internet as the communication platform
VPN concentrator: device that adds support for many tunnels of traffic

## Slide 28
Network Design Techniques (continued)
VPN Protocol
  Point-to-Point Protocol (PPTP)
  Layer 2 Tunneling Protocol (L2TP)
  Secure Socket Tunneling Protocol (SSTP)
  Internet Key Exchange Protocol version 2 (IKEPv2)

## Slide 29
Network Design Techniques (continued)
Point-to-Point Protocol (PPTP): tunneling protocol that provides data confidentiality in the form of encryption, but does not support integrity
Layer 2 Tunneling Protocol (L2TP): tunneling protocol created by Cisco and provides more security than PPTP, but is not as fast

## Slide 30
Network Design Techniques (continued)
Secure Socket Tunneling Protocol (SSTP): tunneling protocol that provides support for traffic over an SSL 3.0-encrypted connection
Internet Key Exchange Protocol version 2 (IKEv2): tunneling protocol that uses the IPSEC tunneling protocol over UDP on port 500

## Slide 31
Network Design Techniques (continued)
VPN Protocol
  Key elements of IPSEC include
    AH (authentication header)
    ESP (encapsulating security payload)
  Tunnel mode encrypts IP headers of original packet
  Transport mode only encrypts data and ESP information

## Slide 32
Network Design Techniques (continued)
VPN Authentication
  Password Authentication Protocol (PAP)
  Challenge Handshake Authentication Protocol (CHAP)
  MS-CHAP
  Extensible Authentication Protocol (EAP)

## Slide 33
Network Design Techniques (continued)
Password Authentication Protocol (PAP): legacy protocol that is not encrypted and should not be used
Challenge Handshake Authentication Protocol (CHAP)
  Protocol in which the server sends a challenge to the client after the client establishes a connection to the server
  Client connection converts to value and sends to VPN server; must match server-calculated value

## Slide 34
Network Design Techniques (continued)

## Slide 35
Network Design Techniques (continued)
MS-CHAP
  Microsoft’s version of CHAP
  Challenge includes a session ID
  Response from client includes session ID, user name, and user password

## Slide 36
Network Design Techniques (continued)

## Slide 37
Network Design Techniques (continued)
Extensible Authentication Protocol (EAP)
  Needed to transport additional authentication data
  Framework for transporting protocols
  Lightweight EAP (LEAP): designed for wireless networking and is based on CHAP protocol
  Protected EAP (PEAP): fully encloses EAP

## Slide 38
Section 9.1 Review
The DNS server that holds the record mapping the host to its IP address is known as what type of DNS server?
Authoritative DNS server
What device is used to create a VLAN?
Switch
A server needing public access should be located in which network location?
DMZ

## Slide 39
Section 9.1 Review
What UDP port must be open for L2TP traffic?
500
If you are going to send biometric information via a VPN, what authentication security protocol must be used?
IPSEC

## Slide 40
Section 9.2
Protecting
Network Devices

## Slide 41
Key Terms
address resolution protocol (ARP)
ARP poisoning
honeynet
honeypot
intrusion-detection system (IDS)
intrusion-prevention system (IPS)
message of the day (MotD)
network access control (NAC)
Network Access Protection (NAP)
System Health Agent (SHA)
unified threat management (UTM)

## Slide 42
Learning Goals
Describe securing network switches.
Discuss securing network routers.
Explain the operation of intrusion-detection systems.
Identify benefits of unified threat management.
Describe access controls on network infrastructure.
Explain how a honeypot acts as a security device.

## Slide 43
Protecting Network Switches
Network switches manage traffic within the subnet
May be Layer 3 switches
Switches are internal to the network
May be overlooked in security configurations

## Slide 44
Protecting Network Switches (continued)
Options for securing switches
  Configure switches so ports can only access specific MAC addresses
  Configure access lists to control traffic in the switch
  Establish secure passwords for console and remote access
  Ensure switches are configured with options such as Spanning Tree protocol

## Slide 45
Protecting Network Switches (continued)
Address resolution protocol (ARP): handles the process of locating addresses in the MAC address table
  Switches maintain a MAC address table
  Used to map an IP address to the physical or MAC address

## Slide 46
Protecting Network Switches (continued)
Goodheart-Willcox Publisher; switch: ridjam/Shutterstock.com; computers: romvo/Shutterstock.com

## Slide 47
Protecting Network Switches (continued)
ARP poisoning: man-in-the-middle attack where a hacker intercepts an ARP request and changes its reply
Victim is pointed to hacker’s computer not the real computer

## Slide 48
Protecting Network Switches (continued)

## Slide 49
Protecting Network Routers
Routers are an integral part of networking environment
Without them, data would be limited to traveling the local subnet.
Play an active role in moving traffic and scanning the network
Must be protected against network hacks

## Slide 50
Protecting Network Routers (continued)
Several steps to keep routers safe:
  Regularly patch all router firmware and router’s operating system
  Secure routers with strong passwords
  Back up all router configuration information
  Ensure that only traffic that should be on subnet is allowed

## Slide 51
Protecting Network Routers (continued)
Several steps to keep routers safe (continued):
  Remind users about security access and responsibilities with router banner
  Check for firmware updates and install only manufacturer patches

## Slide 52
Protecting Network Routers (continued)
Routers manage traffic using Access Control Lists (ACLs)
  Control what is allowed on the subnet
  Security concern: IP spoofing
  ACL can be configured to block any inbound traffic that originates from inside the network

## Slide 53
Protecting Network Routers (continued)
Message of the day (MotD): router banner displayed to user before log-in
Use MotD to provide information on security best practices

## Slide 54
Intrusion-Detection Systems
Intrusion-detection system (IDS)
  Monitors the system and sends an alert if there is a problem
  Host Intrusion Detection System (HIDS)
  Network Intrusion Detection System (NIDS)

## Slide 55
Intrusion-Detection Systems
Intrusion-prevention system (IPS)
  Not only detects malicious or suspicious behavior, it can take action to stop the problem
  Extension of IDS
  Host Intrusion Prevention System (HIPS)
  Network Intrusion Prevention System (NIPS)

## Slide 56
Intrusion-Detection Systems (continued)
Host-based system protects the actual host where it is installed
Network-based solution scans subnet on which it is installed
Goodheart-Willcox Publisher; server: ShendArt/Shutterstock.com; computers: romvo/Shutterstock.com

## Slide 57
Intrusion-Detection Systems
Anomalies
  Network activity is collected
  Establishes a baseline of normal activity
  Variance could be an indication of a threat

## Slide 58
Intrusion-Detection Systems (continued)
Signatures
  IDS identifies traffic or actions different from current known examples
  Signatures are stored and must be frequently updated for comparison
Behavior
  Traffic or actions are examined to see if they are normal
  Something not considered normal will be flagged as a potential risk

## Slide 59
Unified Threat Management
Unified threat management (UTM): appliance that is an all-in-one security device that allows the network to be managed from one location
  Reduces number of devices that must be managed
  Administrators do not have to learn how to use multiple systems
  Can be a lower-cost solution
  Disadvantage: single point of failure or attack

## Slide 60
Network Access Control
Network access control (NAC): environment in which standards are set that hosts must meet before they are able to connect to the network
  Operating system has latest security patches installed
  Antivrius signature files are up-to-date
  Host firewall is turned off
  Approved device

## Slide 61
Network Access Control
Network Access Protection (NAP): Microsoft’s version of an NAC solution
System Health Agent (SHA): agent that performs the self-check on the client
Agent: software or code that searches for vulnerabilities in the client

## Slide 62
Network Access Control (continued)

## Slide 63
Honeypots and Honeynets
Honeypot: decoy server set up to attract hackers
Honeynet: decoy network consisting of two or more honeypots
Reasons to set up a honeypot:
  Learn from hacking techniques used
  Distract hackers
Research honeypot: honeypot set up with the intention of attracting hackers to learn from them and adjust the system

## Slide 64
Honeypots and Honeynets (continued)

## Slide 65
Section 9.2 Review
This protocol resolves an IP address to a MAC address.
ARP
This type of device can spot problems and take immediate steps to mitigate the threat.
intrusion prevention system (IPS)
This all in one device can offer complete security solutions.
Unified Threat Management

## Slide 66
Section 9.2 Review
What is the basic function of a network access control system?
Sets standards that hosts must meet before they are able to connect to the network.
A decoy network designed to watch activity is known as what term?
Honeypot