## Slide 1
Chapter 10
Wireless Network
Security

## Slide 2
Certification Objectives
CompTIA Security+
  1.2 Compare and contrast the types of attacks.
  2.1 Install and configure network components, both hardware and software based, to support organizational security.
  2.2 Given a scenario, use appropriate software tools to assess the security posture of an organization.
  2.3 Given a scenario, troubleshoot common security issues.
  2.5 Given a scenario, deploy mobile devices securely.
  3.3 Given a scenario, implement secure systems design.
  6.3 Given a scenario, install and configure wireless security settings.

## Slide 3
Certification Objectives
Microsoft MTA Security Fundamentals
  1.4 Understand wireless security.
  2.1 Understand user authentication.

## Slide 4
Section 10.1
Wireless
Networking
Overview

## Slide 5
Key Terms
access point (AP)
ANT
basic service set (BSS)
cell
cellular network
dynamic frequency selection (DFS)
extended service set (ESS)
near-field communication (NFC)
satellite communication (SATCOM)
service set identifier (SSID)
Wi-Fi
wireless client (STA)
wireless NIC
wireless router

## Slide 6
Learning Goals
Discuss the state of wireless technologies.
Identify components of a wireless network.
Diagram coverage for a cellular network.
Describe SATCOM and ANT communication methods.

## Slide 7
Review of Wireless Technologies
Wireless technology allows employees to work from anywhere
Increased productivity
Schools are adopting tablets, laptops, and Chromebooks in classes
CTIA
  Trade association representing the wireless-communication industry
  Supports wireless manufacturers and cellular carriers

## Slide 8
Wi-Fi Basics
Wi-Fi: wireless networking technology that uses radio waves instead of wires or fiber optic cable
  Runs on unlicensed bands of the radio frequency (RF) spectrum
  Defined by IEEE 802.11 standard

## Slide 9
Wi-Fi Basics (continued)
Setup
  Typically runs in infrastructure-mode
  Devices must send data to central device before moving on to destination

## Slide 10
Wi-Fi Basics (continued)
Setup
  Requires specific hardware
    Access point (AP)
    Wireless router
    Wireless NIC
    Wireless client (STA)

## Slide 11
Wi-Fi Basics (continued)
Access point (AP): device that provides a central point of access to enable wireless devices to communicate with each other
Wireless router: same capability of an AP, but also adds the functionality of wireless connection to local area networks (LANs) or wide area networks (WANs)

## Slide 12
Wi-Fi Basics (continued)
Wireless NIC: network interface card used to connect the wireless network and may be integrated into a system board or can be added into a system internally or through a USB wireless NIC
Wireless client (STA): fixed or mobile device that has the ability to communicate as a client using the 802.11 standard

## Slide 13
Wi-Fi Basics (continued)
Devices on a wireless network communicate through access points
Basic service set (BSS): wireless network with a single access point
Extended service set (ESS): wireless network with multiple APs
Service set identifier (SSID): name of a wireless network

## Slide 14
Wi-Fi Basics (continued)

## Slide 15
Wi-Fi Basics (continued)
Wireless devices can be manually configured to attach to a wireless network
Another option is Wi-Fi-protected setup (WPS)
  PIN method: user enters PIN on router that is located on new device
  Push method: user pushes button on new device and AP; devices discover each other

## Slide 16
Wi-Fi Basics (continued)
WPS setup methods (continued):
  Near-field communication (NFC): allows devices to communicate through electromagnetic radio fields as opposed to the radio transmissions used by Wi-Fi; user must bring new device close to AP
  USB: user employs USB flash drive with data to copy information between devices
STA finds AP with active or passive scanning

## Slide 17
Wi-Fi Basics (continued)
Interference
  Wireless signals are impacted by many things:
    Surroundings
    Configuration power capability
    Nearby objects and antennae
  Routers transmit power measured in two scales: milliwatt (mW) and decibel-milliwatt (dBm)

## Slide 18
Wi-Fi Basics (continued)
Interference
  Antenna may be omnidirectional or unidirectional
    Omnidirectional: send and receive in all directions
    Unidirectional: send and receive from one specific direction
  Less interference with unidirectional, but often not flexible enough for communication between transmitter and receiver

## Slide 19
Wi-Fi Basics (continued)

## Slide 20
Wi-Fi Basics (continued)
Wireless signals transmit on unlicensed frequencies
802.11 workgroup uses five different frequency ranges:
  2.4 GHz
  3.6 GHz
  4.9 GHz
  5.0 GHz
  5.9 GHz

## Slide 21
Wi-Fi Basics (continued)
Dual-band routers: devices that can be configured to run on multiple frequencies simultaneously
Channels: each of the RF bands is subdivided into slices
Dynamic frequency selection (DFS): detects interference with military and weather radar and automatically shifts the frequency being used by the wireless device

## Slide 22
Cellular Wireless Basics
Cellular network: type of wireless network in which transmissions are distributed over groups of geographic areas
  Transmits data from multiple transmitters called base stations
  Each base station is given a portion of the overall bandwidth
  Cell: coverage provided by the base station

## Slide 23
Cellular Wireless Basics (continued)

## Slide 24
Cellular Wireless Basics (continued)
4G
  G: generation
  Specifications provided by International Telecommunication Union (ITU)
Long-Term Evolution (LTE)
  Path used to provide 4G speeds
  5G expected to be deployed starting 2020

## Slide 25
Cellular Wireless Basics (continued)
Cellular networks operate in licenses areas of RF spectrum
Mobile carriers cannot transmit or receive data using the same frequencies in a given market
FCC tasked with trying to free up additional spectrum

## Slide 26
Additional Wireless Communication Methods
Satellite communication (SATCOM): space-based wireless network in which an orbital satellite provides the connection to the host
  Used for many purposes
  Satellite services can cover entire globe using multiple frequencies
  ITU assigns radio frequencies
  Most used are C, L, and Ku bands

## Slide 27
Additional Wireless Communication Methods (continued)
ANT: personal area technology similar to Bluetooth that allows devices to communicate with each other wirelessly over short distances
  Designed for low-bit, low-power transmissions of small packets
  Used in sports, fitness, and health-care products

## Slide 28
Section 10.1 Review
A _____ is a device that allows connections to a wireless network and can send data to another network.
wireless router
What is an SSID?
The name of a wireless network.
Which channels do not overlap in a 2.4 GHz wireless network?
1, 6, and 11

## Slide 29
Section 10.1 Review
Which governmental agency manages the radio spectrum?
FCC
What is the coverage area of a base station in a cellular network called?
A cell.

## Slide 30
Section 10.2
Wireless
Vulnerabilities

## Slide 31
Key Terms
attenuation
cantenna
data leakage
dead spot
jamming
piggybacking
warchalking
wardriving
wireless site survey

## Slide 32
Learning Goals
Evaluate the placement of a wireless configuration.
Discuss the legal and ethical issues of using someone else’s wireless signal.
Identify security vulnerabilities with wireless routers.
List other peripheral devices that could present vulnerabilities to a wireless network.
Describe the importance of data sniffing on wireless networks.

## Slide 33
Wireless Configuration Placement
Any device that transmits an electromagnetic signal can interfere with RF signals.
Wireless site survey: creates a map of the wireless signal, its strength, and its coverage
  Steps can be taken in regard to placement and configuration
  Should be done on frequent basis as a security measure
  Attenuation: weakening of signal over distance from the access point

## Slide 34
Wireless Configuration Placement (continued)

## Slide 35
Wireless Configuration Placement (continued)
Obstacles can affect signal’s ability to reach destination
Weak signal may make people use less safe ways to communicate
Site surveys can also identify types of equipment in use, approximate locations of equipment, 802.11 standard used, vendor name, and MAC address

## Slide 36
Wireless Configuration Placement (continued)
Dead spot: place where there is no Wi-Fi coverage from a nearby cell
Site survey will find dead spots and indicate strength of signal beyond intended boundaries
Locate access points to provide best coverage of intended area with minimal extension out of building

## Slide 37
Wireless Configuration Placement (continued)

## Slide 38
Wardriving
Wardriving: act of driving around trying to identify wireless networks
  Network names, signal frequencies, and security encryption used
  Can be done by walking, driving, and drones
Warchalking: act of publicly marking locations where network connections are found

## Slide 39
Wardriving (continued)
Many tools available for locating networks and their settings
Hacker trick: use a high-powered antenna
  Can extend physical range of network so hacker can be further away
  Cantenna: homemade device used to amplify Wi-Fi signals
Piggybacking: when a user gains access to a wireless network without permission

## Slide 40
Wardriving (continued)

## Slide 41
Wardriving (continued)
Jamming: intentionally interfering with wireless signals to prevent the transmission from being usable
  Illegal at the state and federal level
  Jammers: RF transmitters that block or scramble other RF signals
  Interferes with all signals

## Slide 42
Router Vulnerabilities
Routers are not immune to flaws
  Change default SSID and password information
  Ensure firmware is up to date
  Change security settings from default
  Replace older routers with new models

## Slide 43
Other Peripheral Vulnerabilities
Devices that access wireless networks pose vulnerabilities
  Wireless keyboard or mouse
  Cameras, printers, microSD cards
Keysniffer
  Hack carried out with what looks like a USB charging device
  Sniffs keystrokes and allows hackers to inject commands or steal information

## Slide 44
Data Sniffing on Wireless Networks
Data leakage: when data are intercepted and stolen
Intrusion-detection or packet-sniffing software can detect vulnerabilities
  Ethical issue: personal information may be read by personnel
  Benefits outweigh privacy concerns
  If data is not protected, hackers will try to access it

## Slide 45
Data Sniffing on Wireless Networks (continued)
Many free or open-source tools for data sniffing
Hacker may insert a rogue access point that has no encryption
  When user connects to AP, requests are transmitted in clear text
  Scripts developed to find unencrypted AP and alert administrators
IoT increased need for oversight of security issues on wireless networks

## Slide 46
Section 10.2 Review
What is a dead spot when discussing a wireless network?
A location in a business without access to Wi-Fi.
Traveling around searching for Wi-Fi networks is called _____.
wardriving
What is it called if you connect to Wi-Fi of a neighbor or nearby business?
piggybacking

## Slide 47
Section 10.2 Review
What does the warchalking symbol )( mean?
open wireless network
List the two most important steps in securing a router.
Changing default SSID and password information.

## Slide 48
Section 10.3
Wireless Access

## Slide 49
Key Terms
authenticator
black listing
Bluejacking
Bluesnarfing
captive portal
censorship
disassociation
enterprise Wi-Fi
evil twin router
initialization vector (IV)
MAC address filtering
man-in-the-middle (MITM) attack
replay attack
rogue router

## Slide 50
Key Terms (continued)
supplicant
white listing
Wired Equivalent Privacy (WEP)
WPA handshake

## Slide 51
Learning Goals
List the three basic encryption choices for protecting data on a wireless network.
Explain MAC address filtering.
Sketch an evil twin router attack.
Compare the function of various captive portals.

## Slide 52
Learning Goals (continued)
Identify security threats to data transfer that uses Bluetooth technology.
Diagram the process for authenticating users under the IEEE 802.1X standard.
Summarize recommendations for wireless security.

## Slide 53
Configuring a Wireless Access Point
Default Settings
  Service set identifier (SSID): default network name for a router
  Default settings are not unique or confidential
  Change default settings on installation
  Always use a strong password

## Slide 54
Configuring a Wireless Access Point (continued)
Encryption
  Security administrator must balance needs against protection
  Three basic choices when protecting data on wireless network
    Leave the network unencrypted
    Offer minimal protection
    Set standards at the highest possible standard

## Slide 55
Configuring a Wireless Access Point (continued)
Unencrypted
  Offers no protection at all
  May be a business need (ex: business provides free Wi-Fi)
  Proper security policies must still be enacted for wireless network
  Censorship: act of limiting access to information or removing information to prevent it from being seen

## Slide 56
Configuring a Wireless Access Point (continued)
Minimal Protection
  Organization may choose to have protection that is not the strongest option available
  Often done to support legacy equipment
  Minimal protection is often easily breakable
  WPA handshake: four-step authentication process used to pass information to and from the WAP and client to set up data encryption

## Slide 57
Configuring a Wireless Access Point (continued)
Strongest Encryption
  Wired Equivalent Privacy (WEP): very outdated encryption protocol for routers used with older, legacy wireless equipment
  Initialization vector (IV): adds random information to the key every time there is a transmission

## Slide 58
Configuring a Wireless Access Point (continued)
Strongest Encryption
  Encryption improved with introduction of Wi-Fi Protected Access (WPA)
  WPA has insecure versions
  WPA encryption variations
    TKIP
    AES

## Slide 59
MAC Address Filtering
Public hotspot: network open to the public
GETMAC command will display MAC addresses embedded into the hardware of network commands in the Physical Address Column
MAC address filtering: limiting which MAC addresses are allowed to access the network

## Slide 60
MAC Address Filtering (continued)

## Slide 61
MAC Address Filtering (continued)
MAC Address Format
  12-digit hexadecimal number
  Two numbers (an octet) separated by a hyphen/dash (-) or a colon (:)
  Consists of six octets
  First three octets represent the organizationally unique identifier (OUI)
  Second three represent a unique address within the vendor’s identifier

## Slide 62
MAC Address Filtering (continued)
Filtering by MAC Address
  Black listing: MAC addresses you do not want connecting to the network are filtered out and blocked from accessing the network
  White listing: MAC addresses you want connecting to the network are filtered in and all other addresses are filtered out and blocked
  MAC filtering won’t keep out a determined hacker
  MAC addresses can be spoofed or faked to allow access

## Slide 63
User Access Security
Man-in-the-middle (MITM) attack: occurs when a hacker intercepts the data transmitted between the client and the WAP
  User is unaware of the attack
  Hacker can gather information such as passwords and user names

## Slide 64
User Access Security (continued)

## Slide 65
User Access Security (continued)
Evil twin router: one that carries the same SSID as the legitimate server, but is a different ESS
  Rogue router is physically placed near the target
  Provides a stronger signal, so victim connects to the evil twin
  Hacker can intercept and discover all data sent to and from target
Rogue router: router that is placed in a business to entice users to connect to it and thus have their credentials stolen

## Slide 66
User Access Security (continued)

## Slide 67
User Access Security (continued)
If user is connected to legitimate router, hacking tools can send disassociation signal
  Disassociation: signal that deactivates the user from the access point
  Stronger signal from evil twin will connect when device reconnects
Replay attack: hacker capturing login credentials during an initial attack, storing them, and retransmitting them at another time

## Slide 68
Captive Portals and Acceptable Use Policies
Captive portal: web page that the user is forced to view before being granted further network access
Landing Target Page
  Can be used for marketing purposes
  Educate users about acceptable use and terms of access
  Collect payment for the service
  Legal protection

## Slide 69
Captive Portals and Acceptable Use Policies (continued)
Acceptable Use Policies
  Set of rules that explain what is and is not allowed on the network
  Employers can display an AUP on a captive portal
  Public Wi-Fi usually requires user to acknowledge AUP before using service

## Slide 70
Bluetooth Security
Bluetooth is a form of wireless networking
  Devices must be physically much closer to each other to communicate
  Ad-hoc networking: devices talk directly to each other
Bluejacking: when somebody sends an unsolicited message via Bluetooth, such as an advertisement
Bluesnarfing: occurs when a hacker exploits the Bluetooth connection to steal data from a Bluetooth-enabled device

## Slide 71
Bluetooth Security (continued)
Steps to take to protect Bluetooth devices and data:
  Turn off Bluetooth when not in use
  User should be extra vigilant in public, crowded areas where the risk of data interception is high
  Use security measures offered on the device

## Slide 72
Enterprise Wi-Fi
Enterprise Wi-Fi: users do not need to be given a passphrase for wireless access
  Authenticated through their network login names and passwords
  Access points pass the credentials and information between the client and authenticating server

## Slide 73
Enterprise Wi-Fi (continued)
Supplicant: computer trying to connect to the WLAN
Authenticator: access point

## Slide 74
Recommendations
Wireless networks must meet the needs of intended audience but also be as secure as possible
Examples of best practices
  Implement strong encryption
  Change default settings
  Limit the availability of the wireless network to posted working hours

## Slide 75
Recommendations (continued)
Examples of best practices (continued)
  Run scripts or other automated tools to discover potential unencrypted data or unauthorized access points
  Use MAC filtering to prohibit access by unapproved devices or disable DHCP so devices must receive a static IP address for access

## Slide 76
Recommendations (continued)
Examples of best practices (continued)
  Set up a captive portal with a security agreement and policy statement before allowing access to the wireless network.
  Require confidentiality agreements from security staff.
  Restrict the websites that can be accessed via wireless networks.

## Slide 77
Recommendations (continued)
Examples of best practices (continued)
  Create strong policies that clearly state acceptable use for users and security staff.
  Require administrators on the wireless network to hold industry certification, such as Certified Wireless Security Professional (CWSP), and to keep it current.

## Slide 78
Recommendations (continued)
Examples of best practices (continued)
  Have clear procedures for reporting lost or stolen equipment.
  Do not allow use of older devices that do not support the latest in encryption technologies.

## Slide 79
Section 10.3 Review
The strongest possible encryption standard is _____.
AES
What are the first three sections of a MAC address called?
OUI
A hacker has placed a router in a business using the same SSID as the business’s wireless access point. What type of attack is this?
Evil twin or man-in-the-middle

## Slide 80
Section 10.3 Review
What type of attack has occurred when unwanted text messages are received on your phone?
Bluejacking
A configuration based on the IEEE 802.1X standard is known as which wireless concept?
Enterprise WiFi